## Slide 1: PLL’s and Phase Noise Modeling in Verilog
Greg Warwar
May 22, 2018

## Slide 2: Outline
  Matrix based circuit solvers
  Clocks and oscillators
  Implementing an oscillator in Verilog
  Implementing an oscillator in Verilog with jitter
  Simulating oscillators in SPICE/Spectre/Eldo
    Accuracy, Simulation Time, Verilog-A, Simulation tool differences
  Phase Lock Loop example in Verilog

## Slide 3: SPICE Circuit Analysis – 3 “nodes”

## Slide 4: SPICE – Another 3-“node” Circuit

## Slide 5: SPICE – Another 3-“node” Circuit
Tolerance settings determine size of “h”
Tolerance also determine accuracy of non-linear elements

## Slide 6: SPICE: Two Non-Coupled Circuits

## Slide 7: SPICE: Two Non-Coupled Circuits – Combined Matrix

## Slide 8: SPICE: Two Non-Coupled Circuits – Combined Matrix
Zeros “fill in” as maxtrix is solved
Uncoupled equations become coupled via numerical roundoff / noise

## Slide 9: Oscillators
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions

## Slide 10: Oscillators
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions
Force an initial condition

## Slide 11: Oscillators – Open Switch 0
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions
Open Switch – signal starts propagating

## Slide 12: Oscillators – Open Switch 1
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions
Open Switch – signal starts propagating

## Slide 13: Oscillators – Open Switch 2
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions
Open Switch – signal starts propagating

## Slide 14: Oscillators – Open Switch 3
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions
Open Switch – signal starts propagating

## Slide 15: Oscillators – Open Switch 4
Delay around ring one time is (6 D)
One period requires going around the ring twice  T = 12 D
The frequency of the oscillator is  f = 1/T
The ring requires an odd number of inversions
Open Switch – signal starts propagating

## Slide 16: Oscillators – How do we simulate in Verilog
D
D
D
D
50ps

## Slide 17: Oscillators – How do we simulate in SPICE
~100ps

## Slide 18: Oscillators – Key Properties
Frequency
  Center frequency  fo
  Frequency range  fmax – fmin
  Frequency vs. Control_Voltage  kv [GHz/V]
Phase
  Phase is the delay of a clock relative to an ideal master
  Phase is measured in [ps], [deg], [rad], [periods]
  Phase is the integral of frequency
Jitter
  Jitter is variation of the phase with time
  Jitter is key performance metric of a precision clock

## Slide 19: Oscillators – (Before Adding Jitter)
D
D
D
D
50ps

## Slide 20: Oscillators – Add Simple Jitter in Verilog – (t = 0)
D
D
D
D
50ps

## Slide 21: Oscillators – Add Simple Jitter in Verilog – (0 < t < 200n)
D
D
D
D
50ps

## Slide 22: Oscillators – Add Simple Jitter in Verilog – (t = 200n)
D
D
D
D
50ps

## Slide 23: Oscillators – Add Simple Jitter in Verilog – (0 < t < 200n)
D
D
D
D

## Slide 24: Why not just use SPICE??
  Isn’t it more accurate?
  Can’t you just put some blocks in “Verilog-A” and go fast?

## Slide 25: Why do we simulate PLL’s and Clocks??
  Study initialization and other transient conditions
  Study interfaces between asynchronous clock domains
    FIFO’s, clock phase alignment circuits
  Study PLL’s in the time domain
    Instability, or “run-away” problems due to nonlinear elements
    Clock recovery circuits with nonlinear control loops
  Verification of top level designs containing PLL’s
  Study jitter generation and propagation

## Slide 26: Intermission - Find your inner self
  Am I an analog or digital guy / gal?

## Slide 27: Intermission - Find your inner self #1

## Slide 28: Intermission - Find your inner self #1
  j  +1 point Analog

## Slide 29: Intermission - Find your inner self #1
  j  +1 point Analog
  i  +1 point Digital

## Slide 30: Intermission - Find your inner self #1
  j  +1 point Analog
  i  +1 point Digital
  ERROR  +2 points Digital

## Slide 31: Intermission - Find your inner self #1
  j  +1 point Analog
  i  +1 point Digital
  ERROR  +2 points Digital
  90°  +2 points Analog

## Slide 32: Intermission - Find your inner self #2
What is the x-axis?

## Slide 33: Intermission - Find your inner self #2
  frequency  +1 point Analog
What is the x-axis?

## Slide 34: Intermission - Find your inner self #2
  frequency  +1 point Analog
  time  +1 point Digital
What is the x-axis?

## Slide 35: Intermission - Find your inner self #2
  frequency  +1 point Analog
  time  +1 point Digital
  cycle  +2 points Digital
What is the x-axis?

## Slide 36: Intermission - Find your inner self #3
What is the units of y-axis?

## Slide 37: Intermission - Find your inner self #3
  dB  +1 point Analog
  volts  +1 point Digital
   +2 points Digital
What is the units of y-axis?
Anything you can count
Errors, hits, collisions, …

## Slide 38: Intermission - Find your inner self #4
What’s wrong with this code?
If (x == 8.3) {
.
.
.
}

## Slide 39: Intermission - Find your inner self #4
  Nothing  +1 point Analog
What’s wrong with this code?
If (x == 8.3) {
.
.
.
}

## Slide 40: Intermission - Find your inner self #4
  Nothing  +1 point Analog
   +1 point Digital
What’s wrong with this code?
If (x == 8.3) {
.
.
.
}
Internal
Roundoff

## Slide 41: Why not just use SPICE??
  Isn’t it more accurate?
  Can’t you just put some blocks in “Verilog-A” and go fast?

## Slide 42: Why do we simulate PLL’s and Clocks??
  Study initialization and other transient conditions
  Study interfaces between asynchronous clock domains
    FIFO’s, clock phase alignment circuits
  Study PLL’s in the time domain
    Instability, or “run-away” problems due to nonlinear elements
    Clock recovery circuits with nonlinear control loops
  Verification of top level designs containing PLL’s
  Study jitter generation and propagation

## Slide 43: What about Verilog-A ????
Looks like Verilog
Language supports triggered events

## Slide 44: What about Verilog-A ????
Looks like Verilog
Language supports triggered events
Still has to be resolved down to a matrix!!!

## Slide 45: Oscillators – Accuracy in SPICE / Spectre / Eldo
~100ps
Benchmark Test
Run 11us
Measure total jitter for (1us < t < 10us)
Tolerance  [conservative, moderate, liberal]

## Slide 46: Oscillators – Accuracy in Eldo - 1
~100ps
F = 7.489851e+08
J = 2.916330e-16
T = 0-min 50-sec

## Slide 47: Oscillators – Accuracy in Eldo - 4
~100ps
F = 7.301669e+08
J = 9.534742e-17
T = 2-min 25-sec

## Slide 48: Oscillators – Accuracy in Eldo - 7
~100ps
F = 7.572305e+08
J = 1.427320e-11
T = 5-min 10-sec*
F = 7.316815e+08
J = 9.628039e-11
T = 5-min 10-sec*

## Slide 49: Oscillators – Accuracy in Eldo - 8
~100ps
F = 7.583032e+08
J = 2.905199e-11
T = 12-min 6-sec*
F = 7.369350e+08
J = 1.422838e-10
T = 12-min 6-sec*
F = 7.681427e+08
J = 1.590278e-10
T = 12-min 6-sec*
F = 7.591970e+08
J = 2.556108e-11
T = 12-min 6-sec*

## Slide 50: Oscillators – Accuracy in Spectre - 1
~100ps
F = 7.530338e+08
J = 2.281258e-12
T = 2-min 18-sec

## Slide 51: Oscillators – Accuracy in Spectre - 2
~100ps
F = 7.538988e+08
J = 1.401772e-12
T = 2-min 18-sec

## Slide 52: Oscillators – Accuracy in Spectre - 3
~100ps
F = 7.540933e+08
J = 1.108888e-11
T = 4-min 23-sec*
F = 7.532945e+08
J = 1.346296e-11
T = 4-min 23-sec*

## Slide 53: Oscillators – Accuracy in Spectre - 4
~100ps
F = 7.697708e+08
J = 5.517425e-18
T = 0-min 49-sec

## Slide 54: Oscillators – Accuracy in Spectre - 5
~100ps
F = 8.067968e+08
J = 3.129376e-18
T = 0-min 58-sec

## Slide 55: Oscillators – Accuracy in Spectre - 6
~100ps
F = 8.067968e+08
J = 1.626288e-15
T = 1-min 56-sec*
F = 7.697708e+08
J = 5.501316e-15
T = 1-min 56-sec*

## Slide 56: Oscillators – Accuracy in Spectre - 7
~100ps
F = 7.551702e+08
J = 6.855988e-13
T = 4-min 47-sec*
F = 7.697708e+08
J = 2.811061e-15
T = 4-min 47-sec*

## Slide 57: Oscillators – Accuracy in Spectre - 8
~100ps
F = 7.558547e+08
J = 9.740328e-12
T = 11-min 5-sec*
F = 7.697708e+08
J = 7.345695e-15
T = 11-min 5-sec*
F = 8.067968e+08
J = 3.472637e-15
T = 11-min 5-sec*
F = 7.567189e+08
J = 7.581477e-12
T = 11-min 5-sec*

## Slide 58: Eldo / Spectre Summary
Eldo has more trouble with Verilog-A
  Verilog-A ~ 3x slower than transistors !!!
  Timing accuracy of Verilog-A is essentially broken
Spectre has better handling of Verilog-A
  Verilog-A ~ 2x faster than transistors
  Timing accuracy of Verilog-A is realiable
  Presence of Verilog-A cells degrades accuracy transistors

## Slide 59: Simulator Types
  Verilog is an event driven simulator
    Time is internally stored as a 64-bit integer.
    `timestep 1ns/1fs
      This indicates that each LSB of time is 1fs
      The user unit of time is 1ns, but internally this is unimportant.
  All events are “snapped” to a simulator time unit.
    Other than “snapping”, no roundoff or numerical error in time calculation
  Spectre, Eldo, HSPICE, (Verilog-A) are timestep simulators
    Timestep simulators do not solve equations exactly
    Iterate until (error < “vntol”)

## Slide 60: Data Types in Verilog
  Time is interally stored as 64-bit integer
    Using 1fs time unit, the largest time possible
      2^64*1fs = 18446 seconds = 5 hr – 7min
  Integers are 32-bit
  Reals and Parameter are double-precision
    ~ 16-digits > 300dB dynamic range
  Use Reals where necessary to avoid “time snapping”
    Especially important in VCO’s and clock sources !!!!

## Slide 61: Verilog Code for Clock Sources

## Slide 62: Verilog Code for Clock Sources

## Slide 63: Verilog Code for Clock Sources
This little bit of code only uses reals to calculate nextTime, which thus has no snapping truncation error

## Slide 64: Noise Model Strategy
  The “$random” verilog function produces a random 32-bit value
  We can make a uniform random value from -227 to 227
    $random % 134217728 (227 = 13417728)
    We can make a gaussian random number with a sigma of 227 by adding 12 of these and dividing by 2. (Scaling by 227 avoids the possibility of overflow when adding 12 of these together.
    Finally, we divide by 227 to get a random value with a sigma of 1.0
  The uniform random variable …
    Has its energy spread evenly from 0 to fs/2. C
    Can be passed through a low pass filter to create white noise with a desired cutoff frequency.
  We model 1/f noise by …
    Use three white noise sources summed in a stair-step fashion
    Typical cutoff frequencies of 100k, 1.0M, and 10.0M

## Slide 76: run1

## Slide 77: run1

## Slide 78: run2

## Slide 79: run2

## Slide 80: Conclusion
  Verilog provides and ideal platform for studying precision timing circuits and systems
  Event driven simulation has significant advantages over an integration based solver (matrix solution)
    Well behaved and easily avoidable round off effects
    Orders of magnitude fasters for long simulations
    Compatible with chip level verification flow
  Verilog-A is similar in appearance to Verilog, but is still resides in the matrix based circuit simulation tools.
    Non-trivial to implement, and robustness varies widely
Thank you!